## Slide 1
Motivation & Introduction
Thermal management has become a pressing issue in 3D-IC design
  High power density caused by complex functionality
  Stacking dies complicates heat dissipation
Designers want to have earlier insights on the effectiveness of thermal management during chip design
Guide cell placement to address potential power-induced thermal issues without doing thermal simulation
Methodology I
Methodology II & Conclusions
Experiments
By inserting appropriately sized WSs based on power distribution analysis, the simulation loop is broken.
Adjusting white space size via lookup tables based on environmental conditions
Unit power thermal response (UPTR) table (Technology dependent)
  Characterize unit power response on thermal behavior considering various geometries
Power-gradient-aware (PGA) cell placement
  Identify hotspot location by coarse and fine grid analyses
  Lookup white space insertion with partition-centering cell replacement
A Novel Power-gradient-aware Cell Placement Methodology Considering 3D-IC Stacking Thermal Boundary to Achieve Timing and Thermal Co-optimization
Hotspot has lateral locality and local similarity
Temperature peaks at the heat source drop drastically
WS: White Space
WSL: Large size
WSM: Medium size
WSS: Small size
UPTR Plot Example
Pre-characterized power-thermal models
  Enable quick identification of hotspot cells.
  Determine necessary white space for heat dissipation.
Foundry process design kits
  Include thermal techfile and RC techfile.
  Allow creation of customized models based on specific needs.
Early design phase considerations
  Ensure adequate space for heat dissipation.
  Avoid iterative thermal simulations.
Notes: 字型大小:48/36/28